## Slide 1
DS Digital Signal Controller
Advance Information
Microchip Technology Inc.
The 16-bit MCU with the power of DSP

## Slide 2: What is DSC ? Digital Signal Control
The DSP Space
8-bit MCU
1 - 10 MIPS
16-bit MCU
5 - 15 MIPS
32-bit MCU
PRICE
PERFORMANCE
Embedded Control
+
Digital Signal Processing
dsPIC30F
The 16-bit MCU with the power of DSP
Notes: I am sure you are wondering, what is Digital Signal Control?
We are all familiar with the 8, 16 and 32 bit MCU segments.
The DSP segment straddles across these MCU markets.
(CLICK FOR ANIMATION)
Digital Signal Control is the convergence of Embedded Control and Digital Signal Processing. An increasing overlap between the MCU and DSP space.
dsPIC30F is Microchip’s first Digital Signal Control family designed specifically for the DSC market.

## Slide 3: dsPIC30F
Looks Like a MCU
Performs Like a DSP
Priced Like a MCU
The 16-bit MCU with the power of DSP

## Slide 4: dsPIC: Architected from scratch
Seamlessly integrates DSP and MCU
MCU look and feel, easy to use
Competitive DSP performance
Optimized for ‘C’ compiler
Fast, deterministic, flexible interrupts
Excellent RTOS support

## Slide 5: Co-Development
Assembler
Simulator
Compiler
DSP
Benchmarks
Compiler
Benchmarks
Applications
dsPIC
Architecture
Definition
MCU
Benchmarks
Verilog Model
Feedback
from Silicon
Design Team
Co-development of Architecture, Compiler, Applications & Algorithms
 In-house compiler team  Motor control consultants
 3rd party compiler vendor  RTOS vendors
 Speech/Modem consultants  Encryption consultants

## Slide 6
Optimized C compiler due to Co-development EEMBC industry std. Benchmarks, Automotive Suite
16-bit Applications
(~ 40KB code)
Mitsubishi M16
Hitachi H8S
Infineon C16X
Motorola HC12
MICROCHIP dsPIC
32-bit Applications
(~ 50KB code)
Mitsubishi M16
Hitachi H8S
Infineon C16X
Motorola HC12
MICROCHIP dsPIC
Relative Code Size
Based on Alpha version of compiler. Further optimization planned.

## Slide 7
dsPIC Architecture Overview
dsPIC30F: 16-bit MCU with the power of DSP

## Slide 8: dsPIC Architectural Highlights
Modified Harvard Architecture
Single Core integrating MCU & DSP
Data path = 16-bit wide
Instruction is 24-bit wide
Linear Program Memory up to: 4M x 24-bit
Linear Data (RAM) up to: 32K x 16-bit
16 x 16 Working Register Array
Software Stack
Fast, deterministic interrupt response
Three operand instructions: A + B = C
Extensive Addressing Modes
True DSP capability

## Slide 9: dsPIC Architectural Highlights
Target Operating Parameters
Target Op Speed: DC - 30 MIPS
  Instruction Cycle: 33 ns
  30 MIPS @ 5V +/- 10%
Target Vdd: 2.5 - 5.5V
Program Memory: Flash
Data Memory: SRAM, EEPROM
Analog: 10 & 12-bit Precision
These are design targets. Final specs will be determined after silicon is characterized.

## Slide 10: dsPIC : Basic Programmers Model
W Registers:
General Purpose
Data Registers
OR
Address Pointers
Stack Pointer
DSP OPERAND
Registers
DSP ADDRESS
Registers
DSP Accumulators
(40-bit)
ACCA
ACCB
Program Counter
(24-bit)
Status Register
0
WREG0
WREG1
WREG2
WREG3
WREG4
WREG5
WREG6
WREG7
WREG8
WREG9
WREG10
WREG11
WREG12
WREG13
WREG14
WREG15
DSP
Status
MCU
Status
15
0
0
15

## Slide 11: dsPIC: Instruction set overview
93 instructions
  Most are one word (24 bit)
  Few are two words
All instructions 1 Cycle, except:
  Program Flow Changes (2 cycles)
  TABLE instructions (2 cycles)
  16-bit literal instructions (2 cycles)
  DO/DOW instructions (2 cycles)
Three operand instructions
  Provides compiler efficiency
  A = B op C
DSP instructions

## Slide 12: dsPIC Architecture overview
Instructions set classes:
  MOVE instructions
  MATH instructions
  LOGIC instructions
  SHIFT instructions
  BIT instructions
  STACK instructions
  PROGRAM FLOW instructions
  CONTROL instructions
  DSP instructions

## Slide 13: Addressing Modes
Generic addressing modes:
  Register W reg array (16)
  Memory Direct 4K words / 8K bytes
  Register Indirect
  Register Indirect with pre-inc or pre-dec
  Register Indirect with post-inc or post-dec
  Literal (Immediate) up to 16 bits
Additional modes for Data Move (mostly for C compiler):
  Register indexed
  Register indirect with signed offset
Special Addressing methods for DSP:
  Modulo (Circular Buffer)
  Bit reverse (for FFT)

## Slide 14: dsPIC30F performance vs. leading 16-bit MCU
* Design Target is 30 MIPS for first dsPIC30F family
Notes: Some basic notes on understanding the data.
1. Instruction Cycle time is the time units in which instruction times are measured. In case of dsPIC it is 1/4 th of the input clock.
3. Average Throughput (MIPS) - Average throughput (MIPS) is somewhat a best guess based upon the published instruction set cycle times. Keep in mind the only way to obtain an accurate timing is to execute a piece of code on each processor and compare the results. As another note, while some devices have a large range, i.e., 1-6 or 2-8, it was determined that a somewhat conservative approach should be used.
Finally, there data for the Toshiba 900 series, National CR16 and ST Super10 was not included in this foil.

## Slide 15: DSP Features (1)
All DSP operations in one cycle
Dual Address Generator Units for two Parallel fetches
  Modulo Addressing: Both AGU
  Bit Reversed Addressing (for FFT): One AGU
16 x 16-bit Fractional/Integer Multiplier
  Supports MCU multiply functions also
Two 40 bit Accumulators with optional saturation
  Less need for data input scaling
  Overflow detect, flags and branches for each Acc
  Supports algorithms using complex values
  Supports two DSP algorithm calculations

## Slide 16: DSP Features (2)
40 stage barrel shifter (+31/-31 shifts)
  Shift Acc, W regs or memory
  Multi-word shift support
Acc Rounding during Memory Store
  Convergent (unbiased) or
  Conventional rounding
Zero Overhead Instruction Loop Support
  REPEAT: Repeat next instruction N times
  DO: Repeat loop N times
  Constant or variable loop count

## Slide 17: dsPIC Architecture Block Diagram
W Array
16 x 16
24-bit PC
Control
DSP Engine
MCU
ALU
Data Memory
(RAM)
32K x 16 bit
DSP: dual access
MCU: single access
X AGU
Y AGU
Instruction
Pre-fetch & Decode
TABLE
Access Cntrl
Address Path
MCU/DSP Data Path
Program Data/Control Path
DSP Data Path
Program
Memory
4M x 24 bit
Linear

## Slide 18: DSP Performance Benchmark
(c) 2001 Berkeley Design Technology Inc.
Cycle Count Comparison (Normalized)
Using Berkley Design Benchmark Suite

## Slide 19: DSP Performance Benchmark
(c) 2001 Berkeley Design Technology Inc.
Execution Time Comparison (Normalized)
Using Berkley Design Benchmark Suite

## Slide 20: Interrupts
Prioritized, vectored interrupts
  Up to 32 sources
  8 levels of priority
  Any interrupt to any priority level
Fixed latency : 3 cycle entry
  Status Register saved
  Instructions to save 2 Wreg in 1 cycle
One ‘non-maskable’ interrupt
Global interrupt enable/disable bit (except traps and interrupts)
DISI instruction suspends interrupts for N cycles
  Quick way to protect critical code segments

## Slide 21: Traps for Robust Operation
Oscillator Failure (switches to Internal RC)
Stack Overflow / underflow
Address Error
  Instruction fetch from unimplemented address space
  Data fetch from unimplemented address space
  Uninitialized W register used as pointer
Arithmetic Error
  Divide by Zero
  Unsaturated Accumulator Overflow
Software Traps for
  Instruction Emulation
  High Priority Software Interrupts

## Slide 22
dsPIC System Integration Features
dsPIC30F: 16-bit MCU with the power of DSP

## Slide 23: System Management Features
Watchdog Timer
  Windowed comparison (optional)
  Only enabled / disabled by “fuse”
  Runs on its own RC oscillator
  Programmable Time out: 2 ms - 16 sec
Power On Reset
Programmable Brown-out Reset
Low Vdd Detect (Interrupt and Reset)

## Slide 24: Clock sources
Instruction Rate = 1/4 of clock rate
Primary Clock Sources:
  Four oscillators for xtal/resonator:
  XTL: 200K - 4 MHz XT: 4 - 10 Mhz
  HS: 10 - 25 MHz LP: 32KHz
  PLL for 4x, 8x and 16x
  PLL output: 16MHz - 160MHz (use XT osc)
  Internal RC oscillator: 7.68 Mhz
  512 KHz RC osc (fail safe clock)
Divide down option on clock: 1:4, 1:16, 1:64
Secondary Clock sources:
  32 KHz Xtal osc from Timer 1 (RTC)

## Slide 25: Clock sources
PLL 4x, 8x, 16x
RC Osc 7.68 Mhz
XT osc
4-10 MHz
XTL osc
200K - 4MHz
HS osc
10 - 25MHz
LP osc
32KHz
OSC1
OSC2
Clock Divide
By
1, 4, 16, 64
32KHz
Timer1 Xtal
OSC
System
Clock
Ext
Xtal
PLL
Secondary Clock source
RC Osc 512 KHz
Low Freq RC
High Freq RC
T1OSC1
T1OSC2

## Slide 26: Power Management Options
Mode Clock CPU Peripherals
Sleep Primary Osc shut down stopped stopped
Pri_Idle Primary Osc running stopped running
RC_Run 512 KHz int RC osc running running
RC_Idle 512 KHz int RC osc stopped running
Sec_Run Secondary 32KHz osc running running

## Slide 27: Fail-safe operation
dsPIC is a very robust MCU
High reliability Watchdog Timer (with own RC osc)
Backup internal clock for crystal failure
Traps for illegal opcodes and addressing
Traps for arithmetic errors
“Safe” data segments in program memory
Boundary checking for Stack

## Slide 28: Security and ID features
dsPIC has excellent Security against code piracy
  Protection of on-chip Flash
  High Security Boot Sector
  Processor is optimized for software encryption
Special field to store “Unique Unit ID”
  Ability to preprogram unique ID at final shipment
  Not erased by chip erase
  Able to access during in-system operation
  Ideal for unique node address
Encryption libraries are planned

## Slide 29
dsPIC FLASH and Data EEPROM
dsPIC30F: 16-bit MCU with the power of DSP

## Slide 30: Flash and EEPROM Memory
Flash memory in our 150K Process (0.5u)
  Uses “PEEC” cell
  Uses Fowler-Nordheim Tunnelling (90A Tunnel oxide)
  Same basic cell for both Flash and EEPROM
Reliability study completed
  Data shows well over 1M cycles at 85C **
  Data retention well over 20 years at 85C **
  Please ask for 150K process Reliability Report
Microchip has 15 years of experience in manufacturing non-volatile memory
** These are preliminary numbers. Please ask for 150K reliability report

## Slide 31: Programming Flash Memory
Production Programming Time:
  ~1 sec / Device
  Independent of Memory size
In-Circuit Serial Programming Mode (ICSP):
  Flash is programmed with the part in the system
  Uses only 2 I/O pins (+ Vdd, Vss, Reset pin)
  Ideal for Programming the part in a Manufacturing Line
  Ideal for “calibration” and “parameterization” & “ID”
Self-Programming:
  can program its own Prog Mem while executing code
  Allows “Remote” update of program code
  Possible to set up secure Boot Segment

## Slide 32
dsPIC30F Peripheral Modules
dsPIC30F: 16-bit MCU with the power of DSP

## Slide 33: dsPIC30F: Planned Peripheral Modules
Timers 16-bit Up to 5
Input Capture Up to 8
Output Compare / PWM Up to 8
Motor Control PWM 6 or 8
A/D converter 10-bit, 500 KSPS, up to 16 ch
A/D converter 12-bit, 100 KSPS, up to 16 ch
UART 1 - 2
SPI 1 - 2
I2C 1
CODEC interface 1
CAN 1 - 2

## Slide 34: Timers / Counters
Up to five 16-bit General Purpose Timers / Counters
Plus BRG, WDT, Motor PWM timebase, QEI
Each timer has
  programmable period register
  prescaler
  Internal / External clock source
Two timers can make a 32-bit timer/counter
Timers are used for Capture / Compare timebase
Timer1 can be a Real-Time Clock
  external 32KHz crystal oscillator
  Can run during SLEEP

## Slide 35: Input Capture
Up to 8 Input Capture pins
Captures 16-bit timer value
  resolution = Instruction Cycle
  At 30 MIPS resolution = 33 ns
4 deep buffer for each capture input
Capture on:
   edge
   edge
  Every 4th  edge
  Every 16th  edge
  Every edge  and 
Wake up from SLEEP

## Slide 36: Output Compare and Standard PWM
Up to 8 Output Compare / PWM Channels
Compare Mode:
  16-bit Compare
  Resolution = Inst. Cycle
  Set, Reset of Toggle Pin
Dual Compare Mode:
  For set and reset, generate Pulse output
  Single or continuous pulse
PWM mode
  16-bit glitch-less (double buffered) PWM output
  Full range of 0 to 100% duty cycle
  Wide frequency Range (very low to very high)
Notes: For the most part the same output compare found on the PIC18Cxxx would be implemented with some additional features such as the variable pulse width generation mode. Currently two interrupts are required or for two compare register writes for generation of a pulse. With a slight enhancement a variable pulse width can be generated with only 1 interrupt. One additional compare register and support logic is added to provide for this mode of operation. In addition a timer reload register (timer period register) is provided which allows for pulses to be generated with a set and continuous time interval between the pulses.
New modes:
Dual compare mode for single output is accomplished by load 2 16-bit compare registers for start and end time of pulse. Start time is relative to timer = 0x0000 start. Enable peripheral and a single pulse will be generated on pin. Pin state can start low and pulse high or start high and pulse low. The period register value must be greater than the end edge compare register value for correct operation.
Dual compare mode for continuous output pulses is accomplished just like above except a continuous stream of pulses is generated.
The net benefit is reduced CPU intervention for the generation of output pulse(s). In addition very short pulses can be generated since no latency is involved for writing to the second compare register as before.
Max resolution specified on bullet 2 is based upon 25MIPS.

## Slide 37: Standard PWM
Standard PWM frequency example:

## Slide 38
Quadrature Encoder Interface
Three Channel Quadrature Encoder Interface
  Two channels for phase A and phase B inputs
  Index pulse input (output from encoder)
Noise filters on inputs
Position measurement modes
  x2 and x4
  Position count register
  Count reset on Index Pulse or Max. Count
Can be used as a General Purpose Timer

## Slide 39: Advanced Motor Control PWM
PWM output: 8 independent or 4 complementary pairs
  3-phase AC Induction
  Brushless DC
  Multi-phase switched-reluctance (SR) motors
Programmable polarity for each output
Programmable Dead-time up to 50us
Output override control for electronic motor commutation
Two external shutdown pins with programmable modes
Can synchronize A/D conversions to PWM

## Slide 40: Advanced Motor Control PWM
Dedicated 16-bit PWM time-base supports:
  Center-aligned or Edge aligned
  Single-pulse PWM
Time-base input prescaler for flexible PWM frequency
PWM interrupt programmable every 1 to 16 cycles
Double-update mode for center-aligned PWM
Notes: The PWM module has a 16-bit timebase and a 16-bit register for each duty cycle.
Features are integrated into the 16-bit PWM time-base to allow center-aligned, edge-aligned, and single-pulse operation. The time-base counts in an up/down mode to generate center-aligned PWM signals. The single-pulse mode allows the time-base to count one period, then stop. This feature is useful for some types of motors.
An edge resolution as small as 33ns can be obtained using the module.
The time-base has an input prescaler to allow very low PWM frequencies at high device speeds.
The time-base has a flexible output postscaler to allow up to a 1:16 divide ratio. This allows the PWM duty cycle updates to occur at a lower frequency than the PWM frequency. Furthermore, a double-update mode can be selected which provides two interrupts per PWM period in center aligned mode. This permits the control loop to be calculated twice per PWM period. Asymmetrical center-aligned waveforms can also be produced.

## Slide 41: Advanced Motor Control PWM
PWM frequency example:

## Slide 42: 10-bit A/D Converter
10 bit Resolution, +/- 1 bit accuracy
500 K Samples / Sec conversion rate
Simultaneous sampling: 4 channels
Up to 16 input channels
External VREF+ and VREF-
Analog Input Range: 0 to 5V (or Vref- to Vref+)
16 deep buffer (Dual port RAM) for A/D result
Automatic scheduled conversion options

## Slide 43: 10-bit A/D Block Diagram
VREF+
VREF-
A D C
10 bit
500 ksps
Conversion
Control
Bus Interface
FIFO
16 deep
Data
Format
Sample
Sequence
Control
Input Muxes
AN0
AN1
S/H
S/H
S/H
S/H
AN15

## Slide 44: 12-bit A/D Converter
12 bit Resolution, +/- 1 bit accuracy
100 K Samples / Sec conversion rate
Up to 16 input channels
External VREF+ and VREF-
Analog Input Range: 0 to 5V (or Vref- to Vref+)
16 deep buffer (Dual port RAM) for A/D result
Automatic scheduled conversion options

## Slide 45: UART
Full Duplex, 8/9 bit
Even, odd or no Parity (with 8-bit data)
1 / 2 Stop bit
Dedicated programmable Baud Rate Generator
4-byte deep transmit buffer
4 byte deep receive buffer
Hardware Flow control support: CTS, RTS
Wake up on address match
Loopback mode for diagnostics

## Slide 46: SPI
8-bit or 16-bit Data
Support ALL Clock polarity / Edge choices
Very wide freq of operation
Dedicated baud rate generator
Framing support to interface to simple Codecs

## Slide 47: I2C
Full Multi Master / Slave implementation
Support 100KHz, 400KHz and 1MHz
Dedicated baud rate generator
SM-bus support

## Slide 48: Codec Interface
Protocols:
  Framed Synchronous Serial Transfer
  AC97 (AC-Link)
  I2S
  TDM (T1/E1)
General Features
  Programmable word size up to 16 bits
  Up to 3 active slots
  Support for up to 16 timeslots
  Support up to 256 bit frame
  Time base for bit clock generator

## Slide 49: CAN
CAN 2.0B
3 Transmit buffers, 2 Receive Buffers
6 full acceptance filters, 2 acceptance masks
Standard and extended data frames
Data length 0-8 bytes
Programmable bit-rates up to 1 Mbps
Support for remote frames
Wake up on CAN message

## Slide 50: dsPIC30F Controller Family
Flash Program Memory: 12 K - 144 K Bytes
RAM 512 - 8 K bytes
Data EEPROM 1 - 4K Bytes
Pin-count 18 - 80 pins
Timers 16-bit Up to 5
Input Capture Up to 8
Output Compare / PWM Up to 8
Motor Control PWM 6 or 8
A/D converter 10-bit, 500 KSPS, up to 16 ch
A/D converter 12-bit, 100 KSPS, up to 16 ch
UART 1 - 2
SPI 1 - 2
I2C 1
CODEC interface 1
CAN 1 - 2

## Slide 51: dsPIC30F Families
Power Conversion and Motor Control Family
Sensor Processor Family
General Purpose Controller Family
dsPIC30F: 16-bit MCU with the power of DSP

## Slide 52: dsPIC30Fxxx Block Diagram
Packages
18 SDIP
20 SSOP
28 SDIP
28 SSOP
40 DIP
44 TQFP
64 TQFP
80 TQFP
MCU / DSP CORE
16-bit ALU
16 x 16 MAC
Dual 40-bit ACC
Program Memory
FLASH
144 K Bytes
Data Memory
SRAM
8 K Bytes
Data Memory
EEPROM
4 K Bytes
TIMER 1
Real Time Clock
16 / 32 bit Timers TIMER 2 / TIMER 3
Quadrature Encoder (TIMER 6)
Motor Control PWM
16-bit, 6-8 ch
Output Compare
Standard PWM
(8 ch / 16-bit)
Input Capture
(8 ch / 16-bit)
UART 1
UART 2
SPI 1
SPI 2
I2C
CODEC interface AC97, I2S
CAN 1
CAN 2
I/O PORTS
ADC 12-bit 100 KSPS
ADC 10-bit 500 KSPS
16 / 32 bit Timers TIMER 4 / TIMER 5
The “Superset / Emulator” Part

## Slide 53: Introduction Approach
Optimized Die
160K (0.4u)
Process
Prod: CQ3 2002 - CQ2 2003
Optimized Die
160K (0.4u)
Process
Prod: CQ3 2002 - CQ2 2003
Longer
Design-in
Cycle
Products
Superset Die
150K (0.5u)
Process
256 Pin QFP
Emulator Part
150K Process
64 / 80 Pin
General Purpose
Controller Variants
64 / 80 Pin
Power Conversion &
Motor Control Variants
Emulator System: CQ1 2002
Sample: CQ1 2002
Sample: CQ1 2002
18 / 28 / 40 Pin Variants
160K (0.4u) Process
Sample: CQ2 onwards Prod: CQ3 2002 - CQ2 2003
Shorter
Design-in
Cycle
Products

## Slide 54: Process Road Map
150K is 0.5u Flash process in production
160K is shrink to 0.4u from 150K process
  Transistors & Flash cell are the same
  Metal / contact is shrunk
  150K to 160K is a low risk transition
  Production early 2002
Next step is 0.25u Flash (Foundry)
  First 8-bit MCU product in development
  Will Support 5V I/O drive, 5V A/D input
  dsPIC products to 0.25u in CY2002 (Prod: 2003)
Microchip also developing internal 0.25u (2003/2004)

## Slide 55
Development Tools
Application Libraries
dsPIC30F: 16-bit MCU with the power of DSP

## Slide 56: Development Tools
MPLAB IDE Integrated Development Free Environment
MPASM Assembler Free
MPSIM Software Simulator Free
MPLAB C30 C Compiler $ 500
MPLAB ICD 2 In Circuit Debugger & $ 200 Device Programmer
MPLAB ICE 4000 In Circuit Emulator $ 3000
PRO MATE 3 Device Programmer $ 800 Production Quality
Prices are preliminary estimates

## Slide 57
Built-In Editor
Project Manager
Source Level Debug
Open Interface
MPLAB Integrated Development Environment
MPASM
Assembler
MPSIM
Software
Simulator
RTOS
OSEK
Linker
Librarian
MPLAB C30
Compiler
ICD 2
In-Circuit
Debugger
ICE 4000
Emulator
PRO MATE 3
PICSTART +
Compilers
IAR, HiTech
Application
Libraries
Languages
Low cost
Debugging
Emulation
Device
Programming
3rd party
Tools

## Slide 58: New MPLAB IDE v6.00
MPLAB Integrated Development Environment
Edit, compile and debug from one IDE
Emulator, Simulator, ICD, Programmer under one IDE
One IDE for PIC and dsPIC controllers
Full featured, syntax color-coding editor
High level language, source code debugging
Mixed C and Assembly debug
Customizable toolbar and key mappings
“State at a glance”, dynamic status bar
Context sensitive, on-line help
One-touch compile and make

## Slide 59: MPLAB v6.00 IDE

## Slide 60: MPLAB SIM Software Simulator
Integrated with MPLAB IDE
Discrete event, instruction based simulator
  Unlimited break points
  Unlimited trace points
  Examine/modify registers
  Watch variables
  Time stamp
Stimulus file injection
Asynchronous stimulus input

## Slide 61
Microchip MPLAB C30 Compiler
dsPIC Architecture and Compiler were co-developed
GNU based optimized compiler
ANSI compliant
Standard libraries, Math libraries
Application specific libraries (planned)
Third Party C Compiler
Two Third Parties developing ANSI C compilers
C Compiler Support

## Slide 62
Optimized C compiler due to Co-development EEMBC industry std. Benchmarks, Automotive Suite
16-bit Applications
(~ 40KB code)
Mitsubishi M16
Hitachi H8S
Infineon C16X
Motorola HC12
MICROCHIP dsPIC
32-bit Applications
(~ 50KB code)
Mitsubishi M16
Hitachi H8S
Infineon C16X
Motorola HC12
MICROCHIP dsPIC
Relative Code Size
Based on Alpha version of compiler. Further optimization expected.

## Slide 63: PRO MATE® Device Programmer
Universal Device Programmer from Microchip
Programs all Microchip Devices
PC Hosted operation under MPLAB
Standalone operation
Suitable for low-volume production
Modular socket modules (sold separately)
Field upgradeable programmer firmware
SQTP Serialization

## Slide 64: MPLAB ICD 2 In-Circuit Debugger
Runs under MPLAB IDE and ICD’s
USB and Serial interface to PC
Flash Programmer
Single Step
Several Breakpoints
  Program
  Data
  Pass count
Very low-cost (< $200)
16,000 ICDs shipped in 2 years

## Slide 65: MPLAB ICE 4000
MPLAB ICE 4000 in-circuit emulator system
Complete, non-intrusive, real-time emulation
Interchangeable processor modules
Support all Microchip MCU’s
Full speed emulation
Low-voltage down to 1.8 volts
32K deep trace memory
Complex break, trace and trigger
Code coverage and statistical performance analysis
Surface mount adapters
USB and parallel port PC interface

## Slide 66: Development Tools & Libraries
Fully Committed
RTOS from several vendors
CAN library
OSEK support
TCP/IP library from multiple vendors
V.22 (2400 bps) soft modem
V.32bis (9600/14.4 Kbps) soft modem
Reference Design for BLDC motor control
Complete Math libraries
DSP algorithm libraries
Visual Filter Design Package
Encryption Libraries

## Slide 67: Development Tools & Libraries
Under Evaluation:
Bluetooth stack
GPS
MP3 player
Speech synthesis
Limited vocabulary recognition
Speaker recognition
Fingerprint recognition
Acoustic noise cancellation

## Slide 68: dsPIC30F: A solid choice for 16-bit MCU
Family of 20+ products
Very High performance MCU
DSP capability for free, when you need it
FLASH reliability is excellent
Analog integration
18-pin to 80-pin offering
Up / down migration in Memory Size
Up / down migration in Pin count
Excellent Security features
C-compiler efficient
Very good Tools at low cost or no cost
Application Libraries and Reference Designs

## Slide 69: dsPIC30F: A solid choice for 16-MCU
Planned Schedule
Full Architecture Disclosure Jun 2001
Software Tool-suite Aug 2001
Samples to Early Adopters Jan 2002
Hardware Tools to Early Adopters Jan 2002
Samples, HW Tools to ALL Customers Apr 2002
Full Production begins CQ3 2002
Contact Microchip if you would like to be an Early Adopter
The 16-bit MCU with the power of DSP

## Slide 70
DS
Digital Signal Controller
The 16-bit MCU with the power of DSP